## Slide 1: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 7: Data Manipulation Instructions
7.1 Arithmetic Instructions (ADD)

## Slide 2: Ch. 7: Data Manipulation Instructions
7.1 Arithmetic Instructions
7.1 Arithmetic instructions
The ALU can be thought of as a collection of combinational logic circuits, each that can perform a desired operation on the data coming from the CPU registers.

## Slide 3: Ch. 7: Data Manipulation Instructions
7.1 Arithmetic Instructions
7.1 Arithmetic instructions
For every operation that is desired when designing the CPU, a new circuit is inserted into the ALU.
The output must be put into either a CPU register or memory.

## Slide 4: Ch. 7: Data Manipulation Instructions
7.1 Arithmetic Instructions
7.1 Arithmetic instructions
ALU has circuits that monitor the operations and produce status flags (or status bits) which are stored in the status register.
The flags are two’s compliment overflow (V), negative (N), zero (Z), and carry (C).
These flags are asserted when the condition exists.
The carry flag can also be used to indicate a borrow when performing subtraction.

## Slide 5: Ch. 7: Data Manipulation Instructions
7.1 Arithmetic Instructions
7.1.1 Addition instructions
add – performs binary addition on two inputs, the src and dst, and puts the sum back into the dst.
Operation can be performed on both 8-bit and 16-bit words by appending .w or .b .
This operation works the same regardless of whether the src or dst are treated as unsigned or signed numbers.
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 6: Ch. 7: Data Manipulation Instructions
7.1 Arithmetic Instructions
7.1.1 Addition instructions

## Slide 7: Ch. 7: Data Manipulation Instructions
7.1 Arithmetic Instructions
Example: Using the ADD instruction
Image Courtesy of
Recording Connection of Canada

## Slide 8: Ch. 7: Data Manipulation Instructions
7.1 Arithmetic Instructions
Example: Using the Addition instruction
Step 1: Create a new Empty Assembly-only CCS project titled:
Asm_ALU_ADD
Step 2: Type in the following code into the main.asm file where the comments say “Main loop here.”
Image Courtesy of
Recording Connection of Canada
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 9: Ch. 7: Data Manipulation Instructions
7.1 Arithmetic Instructions
Example: Using the Addition instruction
Step 3: Debug your program and correct any errors.
Step 4: Set a breakpoint before the first instruction
mov.w #371, R4
Step 5: Open the register viewer and expand the Core Registers item to see the CPU registers. Also expand the status register.
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 10: Ch. 7: Data Manipulation Instructions
7.1 Arithmetic Instructions
Example: Using the Addition instruction
Step 6: Run your program to the breakpoint.
Step 7: Step your program to observe the operation of each addition.
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 11: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 7: Data Manipulation Instructions
7.1 Arithmetic Instructions (ADD)
www.youtube.com/c/DigitalLogicProgramming_LaMeres

## Slide 12: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 7: Data Manipulation Instructions
7.1 Arithmetic Instructions (ADDC = Add with Carry)

## Slide 13: Ch. 7: Data Manipulation Instructions
7.1 Arithmetic Instructions
7.1.1 Addition with Carry instruction
One of the limitations of the add instruction is that it only operates on 16-bit words.
For numbers larger than 16-bit words, we add the lower 16-bit words of the input number first using add, then include the carry that was potentially generated in the addition of the next upper 16-bit words of the inputs.
The addition of higher order words that include the carry from prior additions is repeated until all of the bits in the inputs have been added.
The addc instruction gives us the functionality to include the carry in the addition. src + dst + C → dst

## Slide 14: Ch. 7: Data Manipulation Instructions
7.1 Arithmetic Instructions
Example: Using the Addition with Carry instruction

## Slide 15: Ch. 7: Data Manipulation Instructions
7.1 Arithmetic Instructions
Example: Using the Addition with Carry instruction
Step 1: Create a new Empty Assembly-only CCS project titled:
Asm_ALU_ADDC
Step 2: Type in the following code into the main.asm file where the comments say “Main loop here.”
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 16: Ch. 7: Data Manipulation Instructions
7.1 Arithmetic Instructions
Example: Using the Addition with Carry instruction
Step 3: Debug your program and correct any errors.
Step 4: Set a breakpoint before the first instruction
mov.w #Var1, R4
Step 5: Open the register viewer and expand the Core Register item to see the CPU registers. Also expand the status register. Also go to address 0x2000 in the Memory Browser.
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 17: Ch. 7: Data Manipulation Instructions
7.1 Arithmetic Instructions
Example: Using the Addition with Carry instruction
Step 6: Run your program to the breakpoint.
Step 7: Step your program to observe its operation.
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 18: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 7: Data Manipulation Instructions
7.1 Arithmetic Instructions (ADDC = Add with Carry)
www.youtube.com/c/DigitalLogicProgramming_LaMeres

## Slide 19: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 7: Data Manipulation Instructions
7.1 Arithmetic Instructions (SUB)

## Slide 20: Ch. 7: Data Manipulation Instructions
7.1 Arithmetic Instructions
7.1.2 Subtraction instructions
sub – performs binary addition on two operands and puts the difference back into the dst. dst – src → dst
The operation can be performed on both 8-bit and 16-bit words by appending .w or .b .
The four status flags can be updated.
This operation works the same regardless of whether the src and dst are treated as unsigned or signed numbers.
Image Courtesy of
Recording Connection of Canada
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 21: Ch. 7: Data Manipulation Instructions
7.1 Arithmetic Instructions
7.1.2 Subtraction instructions
The MSP430 does not actually contain a subtraction circuit, instead it converts the src into its negative equivalent by performing two’s compliment on it, and then it adds the src to the dst. A – B = A + (-B)
This explains how the carry flag can be asserted.
When C = 1, then no borrow was required.
When C = 0, then a borrow was required.
Image Courtesy of
Recording Connection of Canada
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 22: Ch. 7: Data Manipulation Instructions
7.1 Arithmetic Instructions
How the Subtraction instruction Works (Ex 1 w/ No Borrow)

## Slide 23: Ch. 7: Data Manipulation Instructions
7.1 Arithmetic Instructions
How the Subtraction instruction Works (Ex 2 w/ Borrow)

## Slide 24: Ch. 7: Data Manipulation Instructions
7.1 Arithmetic Instructions
Example: Using the Subtraction Instruction

## Slide 25: Ch. 7: Data Manipulation Instructions
7.1 Arithmetic Instructions
Example: Using the Subtraction Instruction
Step 1: Create a new Empty Assembly-only CCS project titled:
Asm_ALU_SUB
Step 2: Type in the following code into the main.asm file where the comments say “Main loop here.”

## Slide 26: Ch. 7: Data Manipulation Instructions
7.1 Arithmetic Instructions
Example: Using the Subtraction Instruction
Step 3: Debug your program and correct any errors.
Step 4: Set a breakpoint before the first instruction
mov.b #0FFh, R4
Step 5: Open the register viewer and expand the Core Registers item to see the CPU registers. Also expand the status register.
Step 6: Run your program to the breakpoint.
Step 7: Step your program to observe its operation.

## Slide 27: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 7: Data Manipulation Instructions
7.1 Arithmetic Instructions (SUB)
www.youtube.com/c/DigitalLogicProgramming_LaMeres

## Slide 28: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 7: Data Manipulation Instructions
7.1 Arithmetic Instructions (SUBC = Subtract w/ Carry)

## Slide 29: Ch. 7: Data Manipulation Instructions
7.1 Arithmetic Instructions
7.1.2 Subtraction with Carry instruction
subc – used when subtracting numbers that are larger than 16-bit words. dst – src – not(C) → dst
The subtraction of higher order words that include the borrow from prior subtractions is repeated until all of the bits in the inputs have been subtracted.
Accomplished by subtracting the lower 16-bit words of the input numbers first using sub, and then including the borrow that was potentially generated in the subtraction of the next upper 16-bit words of the inputs.
C = 0 → borrow occurred; C = 1 → no borrow occurred

## Slide 30: Ch. 7: Data Manipulation Instructions
7.1 Arithmetic Instructions
Example: Using Subtraction with Carry Instruction

## Slide 31: Ch. 7: Data Manipulation Instructions
7.1 Arithmetic Instructions
Example: Using Subtraction with Carry Instruction
Step 1: Create a new Empty Assembly-only CCS project titled:
Asm_ALU_SUBC
Step 2: Type in the following code into the main.asm file where the comments say “Main loop here.”
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 32: Ch. 7: Data Manipulation Instructions
7.1 Arithmetic Instructions
Example: Using the Subtraction Instruction
Step 3: Debug your program and correct any errors.
Step 4: Set a breakpoint before the first instruction
mov.w #Var1, R4
Step 5: Open the register viewer and expand the Core Registers item to see the CPU registers. Also expand the status register. Also go to the address 0x2000 in the Memory Browser.
Image Courtesy of
Recording Connection of Canada
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 33: Ch. 7: Data Manipulation Instructions
7.1 Arithmetic Instructions
Example: Using the Subtraction Instruction
Step 6: Run your program to the breakpoint.
Step 7: Step your program to observe its operation.
Image Courtesy of
Recording Connection of Canada
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 34: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 7: Data Manipulation Instructions
7.1 Arithmetic Instructions (SUBC = Subtract w/ Borrow)
www.youtube.com/c/DigitalLogicProgramming_LaMeres

## Slide 35: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 7: Data Manipulation Instructions
7.1 Arithmetic Instructions (Increments and Decrements)

## Slide 36: Ch. 7: Data Manipulation Instructions
7.1 Arithmetic Instructions
7.1.3 Increments and Decrements
Image Courtesy of
Recording Connection of Canada
inc & incd – incremented a storage location by 1 and 2 respectively.
dec & decd – decrements a storage location by 1 and 2 respectively.
Image Courtesy of
Recording Connection of Canada
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 37: Ch. 7: Data Manipulation Instructions
7.1 Arithmetic Instructions
7.1.3 Increments and Decrements
Step 1: Create a new Empty Assembly-only CCS project titled:
Asm_ALU_INC_DEC
Step 2: Type in the following code into the main.asm file where the comments say “Main loop here.”

## Slide 38: Ch. 7: Data Manipulation Instructions
7.1 Arithmetic Instructions
7.1.3 Increments and Decrements
Step 3: Debug your program and correct any errors.
Step 4: Set a breakpoint before the first instruction
mov.w #0, R4
Step 5: Open the register viewer and expand the Core Registers item to see the CPU registers.
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 39: Ch. 7: Data Manipulation Instructions
7.1 Arithmetic Instructions
7.1.3 Increments and Decrements
Step 6: Run your program to the breakpoint.
Step 7: Step your program to observe its operation.
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 40: Ch. 7: Data Manipulation Instructions
7.1 Arithmetic Instructions
7.1.3 Increments and Decrements
Step 8: Now enter the following code. You can place this after the prior inc/dec lines.
Step 9: Debug your program and correct any errors.
Step 10: Step your program to observe its operation.
Step 11: Open the register viewer and memory browsers at 0x2000.
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 41: Ch. 7: Data Manipulation Instructions
7.1 Arithmetic Instructions
7.1.3 Increments and Decrements

## Slide 42: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 7: Data Manipulation Instructions
7.1 Arithmetic Instructions (Increments and Decrements)
www.youtube.com/c/DigitalLogicProgramming_LaMeres

## Slide 43: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 7: Data Manipulation Instructions
7.2 Logic Instructions

## Slide 44: Ch. 7: Data Manipulation Instructions
7.2 Logic Instructions
7.2 Logic Instructions
inv – performs an inversion on each bit of the operand. !dst → dst
and – performs a logical and on the two operands and places the result back into the dst. src AND dst → dst
or – performs a logical or on the two operands and places the result back into the dst. src OR dst → dst
xor – performs an exclusive-or operation on the src and dst and places the result back into the dst. src XOR dst → dst
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 45: Ch. 7: Data Manipulation Instructions
7.2 Logic Instructions
7.2 Logic Instructions
Bitwise operation – takes place on the individual bits of the src and dst independent of each other.
Bit masking – the of setting, clearing, toggling, or testing the value of a bit within a word.
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 46: Ch. 7: Data Manipulation Instructions
7.2 Logic Instructions
7.2 Logic Instructions
Image Courtesy of
Recording Connection of Canada
Bit Masking w/ AND
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 47: Ch. 7: Data Manipulation Instructions
7.2 Logic Instructions
7.2 Logic Instructions
Image Courtesy of
Recording Connection of Canada
Bit Masking w/ AND
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 48: Ch. 7: Data Manipulation Instructions
7.2 Logic Instructions
7.2 Logic Instructions
Bit Masking w/ AND
Image Courtesy of https://neodem.wp.horizon.ac.uk/
Clear
AND’ing anything with a 0 results in a 0.

## Slide 49: Ch. 7: Data Manipulation Instructions
7.2 Logic Instructions
7.2 Logic Instructions
Bit Masking w/ AND
Image Courtesy of https://neodem.wp.horizon.ac.uk/
Clear
AND’ing anything with a 0 results in a 0.
AND’ing anything with a 1 has no impact.

## Slide 50: Ch. 7: Data Manipulation Instructions
7.2 Logic Instructions
7.2 Logic Instructions
Image Courtesy of
Recording Connection of Canada
A “mask” is a set of bits that indicate which bits within a dst are going to be altered depending on the 1s and 0s in the mask.
When using a mask with an AND operation, any position within the mask that contains a 0 will result in the corresponding bit in the dst being cleared.
When using a mask with an AND operation, any position within the mask that contains a 1 will simply leave the original value within the dst.
Example Mask: 00111111
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 51: Ch. 7: Data Manipulation Instructions
7.2 Logic Instructions
7.2 Logic Instructions
Using a mask and an AND operation to clear bits.

## Slide 52: Ch. 7: Data Manipulation Instructions
7.2 Logic Instructions
7.2 Logic Instructions
Image Courtesy of
Recording Connection of Canada
An AND operation with a mask can also check the value of a particular bit(s).
This can be accomplished by using a mask with a 1 in the position of interest and 0’s everywhere else.
The 0’s will be clear all bits except the position of interest.
If the position of interest is a 0, then the entire dst word will be a zero and the Z flag will be asserted (Z = 1).
If the position of interest is a 1, then the entire dst word will NOT be a zero, and the Z flag will not be asserted (Z = 0).
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 53: Ch. 7: Data Manipulation Instructions
7.2 Logic Instructions
7.2 Logic Instructions
Using a mask and an AND operation to test bits.

## Slide 54: Ch. 7: Data Manipulation Instructions
7.2 Logic Instructions
7.2 Logic Instructions
Bit Masking w/ OR
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 55: Ch. 7: Data Manipulation Instructions
7.2 Logic Instructions
7.2 Logic Instructions
Bit Masking w/ OR
Image Courtesy of https://neodem.wp.horizon.ac.uk/
Set
OR’ing anything with a 1 will result in a 1.

## Slide 56: Ch. 7: Data Manipulation Instructions
7.2 Logic Instructions
7.2 Logic Instructions
Bit Masking w/ OR
Image Courtesy of https://neodem.wp.horizon.ac.uk/
Set
OR’ing anything with a 0 has no impact.
OR’ing anything with a 1 will result in a 1.

## Slide 57: Ch. 7: Data Manipulation Instructions
7.2 Logic Instructions
7.2 Logic Instructions
Image Courtesy of
Recording Connection of Canada
A logical OR will produce a 1 when either of the bits of the inputs are a 1. Thus, we can use the OR operation with a one to set any bit within a word.
When using a mask with an OR, the mask indicates which bit(s) to set and which to preserve.
Any position within the mask that contains a 1 will result in the corresponding bit int eh dst being set.
Any position within the mask that contains a 0 will simply leave the original value within the dst.
Example Mask: 00011111
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 58: Ch. 7: Data Manipulation Instructions
7.2 Logic Instructions
7.2 Logic Instructions
Using a mask and an OR operation to set bits.

## Slide 59: Ch. 7: Data Manipulation Instructions
7.2 Logic Instructions
7.2 Logic Instructions
Bit Masking w/ XOR
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 60: Ch. 7: Data Manipulation Instructions
7.2 Logic Instructions
7.2 Logic Instructions
Bit Masking w/ XOR
Image Courtesy of https://neodem.wp.horizon.ac.uk/
Toggle
XOR’ing anything with a 1 will complement the original value.

## Slide 61: Ch. 7: Data Manipulation Instructions
7.2 Logic Instructions
7.2 Logic Instructions
Bit Masking w/ XOR
Image Courtesy of https://neodem.wp.horizon.ac.uk/
Toggle
XOR’ing anything with a 0 has no impact.
XOR’ing anything with a 1 will complement the original value.

## Slide 62: Ch. 7: Data Manipulation Instructions
7.2 Logic Instructions
7.2 Logic Instructions
Image Courtesy of
Recording Connection of Canada
The XOR instruction can be used to toggle bits within the dst.
When XOR’ing a dst bit with a zero, the dst bit will remain unchanged.
To toggle bit(s) in the dst, we simply XOR it with a mask where any bits to be toggled contain a one and all other bits to be preserved are zeros.
Example Mask: 11110000
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 63: Ch. 7: Data Manipulation Instructions
7.2 Logic Instructions
7.2 Logic Instructions
Using a mask and an XOR operation to toggle bits.

## Slide 64: Ch. 7: Data Manipulation Instructions
7.2 Logic Instructions
Example: Logic Instructions to Manipulate Bits
Step 1: Create a new Empty Assembly-only project titled:
Asm_ALU_Logic
Step 2: Type in the following code into the main.asm file where the comments say “Main loop here.”
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 65: Ch. 7: Data Manipulation Instructions
7.2 Logic Instructions
Example: Logic Instructions to Manipulate Bits

## Slide 66: Ch. 7: Data Manipulation Instructions
7.2 Logic Instructions
Example: Logic Instructions to Manipulate Bits
Step 3: Debug your program and correct any errors.
Step 4: Set a breakpoint before the first instruction
mov.b #10101010, R4
Step 5: Open the register viewer and expand the Core Registers item to see the CPU registers. Also expand SR so you can see the Z flag. Change the number format of R4 → R9 to binary.
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 67: Ch. 7: Data Manipulation Instructions
7.2 Logic Instructions
Example: Logic Instructions to Manipulate Bits
Step 6: Run your program to the breakpoint.
Step 7: Step your program to observe its operation.
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 68: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 7: Data Manipulation Instructions
7.2 Logic Instructions
www.youtube.com/c/DigitalLogicProgramming_LaMeres

## Slide 69: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 7: Data Manipulation Instructions
7.3 Bit Set and Bit Clear Instructions

## Slide 70: Ch. 7: Data Manipulation Instructions
7.3 Bit Set and Bit Clear Instructions
7.3 Bit Set and Bit Clear Instructions
bis (bit set) – sets the bits in the dst corresponding to 1’s within the src operand mask.
bic (bit clear) – clears the bits in the dst corresponding to 1’s within the src operand mask.
The bis and bic instructions work on both 16-bit words (.w) and 8-bit bytes (.b).
All bits within the mask for each instruction that are 0’s will leave the dst bits unaltered.
By providing a masking approach that works the same for bis and bic, the same masks can be used throughout the program to alter the same bit location.
Immediate mode is most common.
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 71: Ch. 7: Data Manipulation Instructions
7.3 Bit Set and Bit Clear Instructions
Example: Using BIS and BIC to Set & Clear Bits
Step 1: Create a new Empty Assembly-only project titled:
Asm_ALU_BIS_BIC
Step 2: Type in the following code into the main.asm file where the comments say “Main loop here.”

## Slide 72: Ch. 7: Data Manipulation Instructions
7.3 Bit Set and Bit Clear Instructions
Example: Using BIS and BIC to Set & Clear Bits
Step 3: Debug your program and correct any errors.
Step 4: Set a breakpoint before the first instruction
mov.b #00000000b, R4
Step 5: Open the register viewer and expand the Core Registers item to see the CPU registers. Change the number format of R4 to binary.
Step 6: Run your program to the breakpoint.
Step 7: Step your program to observe its operation.

## Slide 73: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 7: Data Manipulation Instructions
7.3 Bit Set and Bit Clear Instructions
www.youtube.com/c/DigitalLogicProgramming_LaMeres

## Slide 74: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 7: Data Manipulation Instructions
7.4 Test Instructions

## Slide 75: Ch. 7: Data Manipulation Instructions
7.4 Test Instructions
7.4 Test Instructions
Image Courtesy of
Recording Connection of Canada
Testing a bit or word – try to determine whether a bit is one, whether the value is zero, whether the values is negative, or whether the value is the same as another number.
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 76: Ch. 7: Data Manipulation Instructions
7.4 Test Instructions
7.4 Test Instructions
Image Courtesy of
Recording Connection of Canada
Bit (bit test) – perform a logical AND with the mask provided in the src and the value held in the dst.
This is used to determine whether certain bits within the dst are 1’s by checking the Z flag after the operation.
If the bit location in the dst dictated by the mask is a 1, then the result of the AND will be value that is not zero and the Z flag will not be asserted (Z = 0).
If the Z flag is asserted (Z = 1), then the bit value of interest in the dst was a zero.
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 77: Ch. 7: Data Manipulation Instructions
7.4 Test Instructions
7.4 Test Instructions
Image Courtesy of
Recording Connection of Canada
Cmp (compare) – subtracts the src from the dst and updates the status flags, but leaves the dst intact.
This is used to determine if the dst is equal to a specific value by checking the Z flag after the operation.
If the src and dst are equal, the result of the subtraction will result in zero, and the Z flag will be asserted (Z = 1).
If the Z flag is not asserted (Z = 0), then src and dst were not the same.
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 78: Ch. 7: Data Manipulation Instructions
7.4 Test Instructions
7.4 Test Instructions
Image Courtesy of
Recording Connection of Canada
Tst (test)– subtracts zero form the dst and updates the status flags.
This instruction allows us to determine whether the value in the dst is zero (Z = 1) or negative (N = 1).
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 79: Ch. 7: Data Manipulation Instructions
7.4 Test Instructions
7.4 Test Instructions
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of https://neodem.wp.horizon.ac.uk/
Step 1: Create a new Empty Assembly-only project titled:
Asm_ALU_TESTS
Step 2: Type in the following code into the main.asm file where the comments say “Main loop here.”

## Slide 80: Ch. 7: Data Manipulation Instructions
7.4 Test Instructions
7.4 Test Instructions
Step 3: Debug your program and correct any errors.
Step 4: Set a breakpoint before the first instruction
mov.b #00010000b, R4
Step 5: Open the register viewer and expand the Core Registers item to see the CPU registers. Change the number format of R4 to binary and R5/R6 to decimal.
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 81: Ch. 7: Data Manipulation Instructions
7.4 Test Instructions
7.4 Test Instructions
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Step 6: Run your program to the breakpoint.
Step 7: Step your program to observe its operation.
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 82: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 7: Data Manipulation Instructions
7.4 Test Instructions
www.youtube.com/c/DigitalLogicProgramming_LaMeres

## Slide 83: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 7: Data Manipulation Instructions
7.5 Rotate Operations

## Slide 84: Ch. 7: Data Manipulation Instructions
7.5 Rotate Operations
7.5 Rotate Operations
Rotate instructions - used to shift in serial data into a parallel word, to sign extend negative numbers, or to perform multiply/divide by two operations.

## Slide 85: Ch. 7: Data Manipulation Instructions
7.5 Rotate Operations
Example: Using Rotate Arithmetically
Step 1: Create a new Empty Assembly-only project titled:
Asm_ALU_ROTATE_ARITH
Step 2: Type in the following code into the main.asm file where the comments say “Main loop here.”
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of https://neodem.wp.horizon.ac.uk/
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 86: Ch. 7: Data Manipulation Instructions
7.5 Rotate Operations
Example: Using Rotate Arithmetically

## Slide 87: Ch. 7: Data Manipulation Instructions
7.5 Rotate Operations
Example: Using Rotate Arithmetically
Step 3: Debug your program and correct any errors.
Step 4: Set a breakpoint before the first instruction
mov.b #00000001b, R4
Step 5: Open the register viewer and expand the Core Registers item to see the CPU registers. Change the number format of R4 → R5 to binary. Expand SR so you can see the C-flag.
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of https://neodem.wp.horizon.ac.uk/
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 88: Ch. 7: Data Manipulation Instructions
7.5 Rotate Operations
Example: Using Rotate Arithmetically
Step 6: Run your program to the breakpoint.
Step 7: Step your program to observe its operation.
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of https://neodem.wp.horizon.ac.uk/
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 89: Ch. 7: Data Manipulation Instructions
7.5 Rotate Operations
Example: Using Rotate Through Carry
Step 1: Create a new Empty Assembly-only project titled:
Asm_ALU_ROTATE_THRC
Step 2: Type in the following code into the main.asm file where the comments say “Main loop here.”
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of https://neodem.wp.horizon.ac.uk/
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 90: Ch. 7: Data Manipulation Instructions
7.5 Rotate Operations
Example: Using Rotate Through Carry

## Slide 91: Ch. 7: Data Manipulation Instructions
7.5 Rotate Operations
Example: Using Rotate Through Carry
Step 3: Debug your program and correct any errors.
Step 4: Set a breakpoint before the first instruction
mov.b #00000001b, R6
Step 5: Open the register viewer and expand the Core Registers item to see the CPU registers. Change the number format of R6 → R7 to binary. Expand SR so you can see the C-flag.
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of https://neodem.wp.horizon.ac.uk/
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 92: Ch. 7: Data Manipulation Instructions
7.5 Rotate Operations
Example: Using Rotate Through Carry
Step 6: Run your program to the breakpoint.
Step 7: Step your program to observe its operation.
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of https://neodem.wp.horizon.ac.uk/
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 93: Ch. 7: Data Manipulation Instructions
7.5 Rotate Operations
7.5 Rotate Operations
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of https://neodem.wp.horizon.ac.uk/
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of https://neodem.wp.horizon.ac.uk/
Rotate instructions - perform multiply/divide by two operations.
When a binary number is rotated to the left by one bit and the vacated LSB position is filled with a zero, it doubles the original value.
When a binary number is rotated to the right by one bit and the vacated MSB position is filled with a zero.

## Slide 94: Ch. 7: Data Manipulation Instructions
7.5 Rotate Operations
Example: Using Rotate to Multiply and Divide by 2
Step 1: Create a new Empty Assembly-only project titled:
Asm_ALU_MUL2_DIV2
Step 2: Type in the following code into the main.asm file where the comments say “Main loop here.”
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of https://neodem.wp.horizon.ac.uk/
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 95: Ch. 7: Data Manipulation Instructions
7.5 Rotate Operations
Example: Using Rotate to Multiply and Divide by 2

## Slide 96: Ch. 7: Data Manipulation Instructions
7.5 Rotate Operations
Example: Using Rotate to Multiply and Divide by 2
Step 3: Debug your program and correct any errors.
Step 4: Set a breakpoint before the first instruction
mov.b #25, R8
Step 5: Open the register viewer and expand the Core Registers item to see the CPU registers. Change the number format of R8 → R9 to decimal.
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of https://neodem.wp.horizon.ac.uk/
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 97: Ch. 7: Data Manipulation Instructions
7.5 Rotate Operations
Example: Using Rotate to Multiply and Divide by 2
Step 6: Run your program to the breakpoint.
Step 7: Step your program to observe its operation.
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of https://neodem.wp.horizon.ac.uk/
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 98: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 7: Data Manipulation Instructions
7.5 Rotate Operations
www.youtube.com/c/DigitalLogicProgramming_LaMeres