## Slide 1: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 10: The STACK and Subroutines
10.1 The STACK

## Slide 2: Ch. 10: The STACK and Subroutines
10.1 The STACK
10.1 the Stack
A stack is a last-in, first out (LIFO) storage structure.

## Slide 3: Ch. 10: The STACK and Subroutines
10.1 The STACK
10.1 the Stack
Stack – a system that allows us to dynamically allocate data memory.
Dynamically – we can access memory without initializing it or reserving it using assembler directives such as .short and .space.

## Slide 4: Ch. 10: The STACK and Subroutines
10.1 The STACK
10.1 the Stack
What Physically is the Stack in an MCU?
  Storage at the end of data memory & an address pointer.

## Slide 5: Ch. 10: The STACK and Subroutines
10.1 The STACK
10.1 the Stack
The data memory range in the MSP430FR2355 is from 2000h → 2FFFh.
The stack resides at the end of data memory to allow the maximum potential size of the stack and also avoids overriding reserved locations in memory that are placed at the beginning address of data memory (i.e., 2000h).
SP

## Slide 6: Ch. 10: The STACK and Subroutines
10.1 The STACK
10.1 the Stack
SP is initialized to 3000h.
This means that the first 16-bit word of information pushed will be stored at address 2FFEh.
This is accomplished using a move instruction and a global constant called __STACK_END.
SP

## Slide 7: Ch. 10: The STACK and Subroutines
10.1 The STACK
10.1 the Stack
Push = Put Data on Stack - decrement SP - dst  @SP
Pop = Get Data from Stack - increment SP - mov src, @SP
SP

## Slide 8: Ch. 10: The STACK and Subroutines
10.1 The STACK
10.1 the Stack
Push = Put Data on Stack - decrement SP - dst  @SP - .w: SP – 2  SP
Pop = Get Data from Stack - increment SP - mov src, @SP - .w: SP + 2  SP
SP

## Slide 9: Ch. 10: The STACK and Subroutines
10.1 The STACK
10.1 the Stack

## Slide 10: Ch. 10: The STACK and Subroutines
10.1 The STACK
10.1 the Stack
STACK Overflow
  When pushes start overwriting other locations in memory.
SP

## Slide 11: Ch. 10: The STACK and Subroutines
10.1 The STACK
Example: Using the Stack

## Slide 12: Ch. 10: The STACK and Subroutines
10.1 The STACK
Example: Using the Stack
Image Courtesy of
Recording Connection of Canada
Step 1: Create a new Empty Assembly-only CCS project titled:
Asm_Stack
Step 2: Type in the following code into the main.asm file where the comments say “Main loop here.”
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 13: Ch. 10: The STACK and Subroutines
10.1 The STACK
Example: Using the Stack
Image Courtesy of
Recording Connection of Canada
Step 3: Debug your program.
Step 4: Run your program to the breakpoint.
Step 5: Open the Register Viewer so that you can see SP and R4 → R7. Open the Memory Browser and go to 0x3000. Then scroll up so you can see the values 2FFEh and 2FFCh.
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 14: Ch. 10: The STACK and Subroutines
10.1 The STACK
Example: Using the Stack
Step 6: Step your program. As you step, look at the values of SP and the values in data memory before 0x3000. In the Memory Browser you should see the following as the values are pushed.

## Slide 15: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 10: The STACK and Subroutines
10.1 The STACK
www.youtube.com/c/DigitalLogicProgramming_LaMeres

## Slide 16: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 10: The STACK and Subroutines
10.2 Subroutines

## Slide 17: Ch. 10: The STACK and Subroutines
10.2 Subroutines
10.2 Subroutines
Subroutine – a piece of code that will be used repeatedly in a program; typically accomplishes a very specific task.
The subroutine code is implemented only once outside the main program loop. This creates a more efficient and simple program to read.
Other names for subroutines: procedures, functions, routines, methods, subprograms.
Main Program
Subroutine 1
Subroutine 2

## Slide 18: Ch. 10: The STACK and Subroutines
10.2 Subroutines
10.2 Subroutines
Whenever the subroutine is needed, it can be executed by jumping to it.
Once the subroutine completes, a return jump is used to move the PC back to the next location in the main program loop to continue operation.
Main Program
Subroutine 1
Subroutine 2

## Slide 19: Ch. 10: The STACK and Subroutines
10.2 Subroutines
10.2 Subroutines
A subroutine starts with an address label to mark its location in memory.
Additional steps must be taken when jumping to a subroutine because while the starting address of the subroutine is always the same, the return address in the main program will vary depending on where in the main program it is called.
Main Program
Subroutine 1
Subroutine 2

## Slide 20: Ch. 10: The STACK and Subroutines
10.2 Subroutines
10.2 Subroutines
Call – instruction that is used to jump to the subroutine address label and handles storing the return address on the stack prior to jumping to the subroutine address.
Ret – instruction used at the end of the subroutine that pops the return address off the stack and places it into PC to return to the main program.
Main Program
Subroutine 1
Subroutine 2

## Slide 21: Ch. 10: The STACK and Subroutines
10.2 Subroutines
10.2 Subroutines
Variables can be passed to subroutines using three different approaches:
  Using the CPU registers
  Using the stack
  Using dedicated variables in data memory
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 22: Ch. 10: The STACK and Subroutines
10.1 The STACK
Example: Using Subroutines

## Slide 23: Ch. 10: The STACK and Subroutines
10.2 Subroutines
Example: Using Subroutines
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Step 1: Create a new Empty Assembly-only CCS project titled:
Asm_Subroutines
Step 2: Type in the following code into the main.asm file where the comments say “Main loop here.”
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 24: Ch. 10: The STACK and Subroutines
10.1 The STACK
Example: Using Subroutines
Image Courtesy of
Recording Connection of Canada
Step 3: Debug your program.
Step 4: Run your program to the breakpoint.
Step 5: Open the Register Viewer so that you can see PC, SP, and R4. Open the Memory Browser and go to 0x3000. Then scroll up so you can see the first location on the stack (address 2FFEh).
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 25: Ch. 10: The STACK and Subroutines
10.1 The STACK
Example: Using Subroutines
Step 6: Step your program using Step Into. As you step, look at the values of PC, SP, and the values in data memory for the stack. In the Memory Browser you should see the following as the values are pushed.
Step 7: Now step your program using Step Over. This time when you step you’ll see the program still executes the subroutine, but it doesn’t move into the subroutine code. This is the first time we have been able to use step over.

## Slide 26: Ch. 10: The STACK and Subroutines
10.1 The STACK
Example: Using Subroutines
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 27: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 10: The STACK and Subroutines
10.2 Subroutines
www.youtube.com/c/DigitalLogicProgramming_LaMeres