## Slide 1: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 14: Serial Communications in C
14.1 Serial Communications Overview

## Slide 2: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
Parallel Communication – How we send information as a full word using the MCU ports. a full word.

## Slide 3: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
Serial Communication – uses a single wire to send information between a transmitter (Tx) and a receiver (Rx) as a sequence of bits.
Serial communication allows information to be transmitted using less pins compared to parallel communication, but at a slower overall information transmission rate due to only sending one bit at a time as opposed to a full word.

## Slide 4: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
Serial Communications on MCU’s

## Slide 5: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
Serial Communications on MCU’s - Method 1 – “Bit Banging” - use BIC and BIS instructions to send the desired pattern out of a port pin. - Timer IRQs are used to set the data and clock periods.

## Slide 6: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
Serial Communications on MCU’s - Method 1 – “Bit Banging” - Method 2 – “Built in Serial Peripherals” - enhanced Universal Serial Communication Interfaces (eUSCI). - The MSP430FR2355 contains four eUSCI peripherals (eUSCI_A0, eUSCI_A1, eUSCI_B0, eUSCI_B1)

## Slide 7: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
MSP430FR2355 serial communication standards:
  Universal Asynchronous Receiver/Transmitter (UART)
  Serial Peripheral Interface (SPI)
  Inter-integrated circuits (I2C) protocol

## Slide 8: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
Serial Communications on MCU’s - Method 1 – “Bit Banging” - Method 2 – “Built in Serial Peripherals”

## Slide 9: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Parallel-to-Serial Concept (Tx)
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of https://neodem.wp.horizon.ac.uk/
Parallel Register
Tx

## Slide 10: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Serial-to-Parallel Concept (Tx)
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of https://neodem.wp.horizon.ac.uk/
Parallel Register
Rx

## Slide 11: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
Serial Communications on MCU’s - Learning…. Step 1 – you need to know the standard. Step 2 – decide whether to bit bang or use peripheral. We will use the peripherals. After you see the serial busses in action, bit banging will make more sense.

## Slide 12: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 14: Serial Communications in C
14.1 Serial Communications Overview
www.youtube.com/c/DigitalLogicProgramming_LaMeres

## Slide 13: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 14: Serial Communications in C
14.1.1 The UART Standard

## Slide 14: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
14.1.1 The UART Standard
Universal asynchronous receiver/transmitter – an approach to serial communication between two devices in which neither device shares a common clock.
Each device only uses lines for data.
Has a predefined protocol for how data is framed, how data packets start and stop, and how the receiver oversamples the incoming data to recover the information sent.

## Slide 15: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
14.1.1 The UART Standard
Baud rate (BR) – the common data rate between Tx and Rx; the fastest rate at which the data line changes states.
The baud rate and bit period (TB) are related by BR = 1/TB.
Baud rate must be set manually in both the Tx and Rx prior to data transmission (typical range is 9600 to 115200 baud).

## Slide 16: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
14.1.1 The UART Standard
Link – when two devices are connected together to transfer information.

## Slide 17: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
14.1.1 The UART Standard
Framing – the term used to describe how the bits are arranged in the UART serial bit sequence.

## Slide 18: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
14.1.1 The UART Standard
Framing – the term used to describe how the bits are arranged in the UART serial bit sequence.
Having the Tx drive a HIGH while not transmitting tells the Rx that it is still powered on.

## Slide 19: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
14.1.1 The UART Standard
Framing – the term used to describe how the bits are arranged in the UART serial bit sequence.
Start bit – initial symbol
To start a data transmission, the Tx drives the line LOW and holds it there for one TB.

## Slide 20: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
14.1.1 The UART Standard
The data word is transmitted bit-by-bit, typically starting with the LSB.

## Slide 21: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
14.1.1 The UART Standard
Stop bit – last symbol
After the bits have been transmitted, the Tx drives the line HIGH for one TB to represent the end of the sequence.

## Slide 22: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
14.1.1 The UART Standard
The most common options that are configurable on the MSP430 are swapping the order in which the bits are sent, changing the data size between 7-bits and 8-bits, adding on address bit (AD), adding a parity bit (PA), and adding a second stop bit.

## Slide 23: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
14.1.1 The UART Standard
When using a transmit address, two frames are sent, one for data and one for address.
The AD bit signifies whether the next frame is the address or data.

## Slide 24: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
14.1.1 The UART Standard
The addition of a second stop bit can be used to provide extra time between packets when running at higher baud rates in order to make the link more reliable.

## Slide 25: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
14.1.1 The UART Standard
Parity bit – used to detect transmission errors.
Even parity – the transmitter counts the number of 1’s in the data word and if the count is odd, it asserts the parity bit.
Odd parity – the transmitter counts the number of 1’s in the data word and if the count is even, it asserts the parity bit.

## Slide 26: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
14.1.1 The UART Standard
How does the receiver determine what logic is sent if it doesn’t have a clock?
Oversampling – using a receiver clock that is faster than the transmitter clock
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 27: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
14.1.1 The UART Standard

## Slide 28: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
14.1.1 The UART Standard

## Slide 29: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
14.1.1 The UART Standard
Communication standard – when logic levels are assigned to the UART logic values.
As standard allows separate devices to communicate because both the logic levels and packet structure are known.
The term transistor-to-transistor logic (TTL) is used to describe a UART that transmits a HIGH as the power supply (Vcc) of the device and a LOW as the GND of the device.
MSP430FR2355 Specifications: Uses +3.4v TTL
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 30: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
14.1.1 The UART Standard

## Slide 31: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 14: Serial Communications in C
14.1.1 The UART Standard
www.youtube.com/c/DigitalLogicProgramming_LaMeres

## Slide 32: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 14: Serial Communications in C
14.1.2 UART Transmit on the MSP430FR2355 - Configuration

## Slide 33: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
14.1.2 UART Transmit on the MSP430FR2355
The MSP430FR2355 contains two eUSCIs that support UARTs, eUSCI_A0 and eUSCI_A1.

## Slide 34: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
14.1.2 UART Transmit on the MSP430FR2355
The basic concept of operation of the UART system is to first configure its baud rate and frame characteristics.

## Slide 35: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
14.1.2 UART Transmit on the MSP430FR2355
We then store the data to be transmitted into a Tx buffer register, and a shift register will automatically send the data out over the Tx pin in a serial pattern.

## Slide 36: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
14.1.2 UART Transmit on the MSP430FR2355
The UART can also produce a variety of interrupts such as data received, transmit complete, and many others used for detecting transmission errors.

## Slide 37: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
14.1.2 UART Transmit on the MSP430FR2355
Steps to Configure the UART Peripheral:
Step 1: Set the UCSWRST bit in the UCAxCTLW0 configuration register to put the eUSCI_Ax peripheral into reset. Note that the default value for UCSWRST = 1 on system power-on or system reset, so the system is initially in software reset.
Step 2: Initialize all eUSCI_Ax configuration registers.
Step 3: Configure ports.
Step 4: Clear UCSWRST to take the eUSCI_Ax peripheral out of reset.
Step 5: Enable interrupts (optional) using the UCRXIE or UCTXIE bits int eh UCAxIE configuration register.

## Slide 38: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
14.1.2 UART Transmit on the MSP430FR2355
eUSCI_Ax Control Word 0 (UCAxCTLW0)
eUSCI_Ax Control Word 1 (UCAxCTLW1)
eUSCI_Ax Baud Rate Control Word (UCAxBRW)
eUSCI_Ax Modulation Control Word (UCAxMCTLW)
eUSCI_Ax Status (UCAxSTATW)
eUSCI_Ax Receive Buffer (UCAxRXBUF)
eUSCI_Ax Transmit Buffer (UCAxTXBUF)
eUSCI_Ax Auto Baud Rate Control (UCAxABCTL)
eUSCI_Ax IrDA Control (UCAxIRCTL)
eUSCI_Ax Interrupt Enable (UCAxIE)
eUSCI_Ax Interrupt Flag (UCAxIFG)
eUSCI_Ax Interrupt Vector (UCAxIV)

## Slide 39: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
14.1.2 UART Transmit on the MSP430FR2355
We can start by just looking at the bare minimum to get the UART setup.

## Slide 40: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
14.1.2 UART Transmit on the MSP430FR2355
We can start by just looking at the bare minimum to get the UART setup.
The UCAxCTLW0 register has a LOT of our settings.

## Slide 41: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
14.1.2 UART Transmit on the MSP430FR2355
We can start by just looking at the bare minimum to get the UART setup.
The UCAxCTLW0 register has a LOT of our settings.
First, let’s consider what the default settings out of reset are:

## Slide 42: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
14.1.2 UART Transmit on the MSP430FR2355
We can start by just looking at the bare minimum to get the UART setup.
The UCAxCTLW0 register has a LOT of our settings.
First, let’s consider what the default settings out of reset are: - We’re by default in UART mode.

## Slide 43: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
14.1.2 UART Transmit on the MSP430FR2355
We can start by just looking at the bare minimum to get the UART setup.
The UCAxCTLW0 register has a LOT of our settings.
First, let’s consider what the default settings out of reset are: - We also have standard framing options.

## Slide 44: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
14.1.2 UART Transmit on the MSP430FR2355
We can start by just looking at the bare minimum to get the UART setup.
The UCAxCTLW0 register has a LOT of our settings.
First, let’s consider what the default settings out of reset are: - The UCSWRST bit is where we enable/disable the UART. - We need to put into Reset to configure the UART. - Note we “enable” a reset with UCSWRST=1

## Slide 45: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
14.1.2 UART Transmit on the MSP430FR2355
We can start by just looking at the bare minimum to get the UART setup.
The UCAxCTLW0 register has a LOT of our settings.
First, let’s consider what the default settings out of reset are: - We can choose our clock source using the UCSSELx bits. - We usually use ACLK or SMCLK.

## Slide 46: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
14.1.2 UART Transmit on the MSP430FR2355
We can start by just looking at the bare minimum to get the UART setup.
The UCAxCTLW0 register has a LOT of our settings.
First, let’s consider what the default settings out of reset are: - There are also options for error handling. - We won’t be using these.

## Slide 47: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
14.1.2 UART Transmit on the MSP430FR2355
The eUSCI_Ax peripheral has a baud rate generation circuit that can produce standard baud rates from nonstandard clock sources such as SMCLK (1MHz) and ACLK (32.768kHz).
The baud rate is set using two configuration registers, the eUSCI_Ax Baud Rate Control Word (UCAxBRW) and eUSCI_Ax Modulation Control Word (UCAxMCTLW) regsiters.

## Slide 48: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
14.1.2 UART Transmit on the MSP430FR2355
The eUSCI_Ax peripheral has a baud rate generation circuit that can produce standard baud rates from nonstandard clock sources such as SMCLK (1MHz) and ACLK (32.768kHz).
The baud rate is set using two configuration registers, the eUSCI_Ax Baud Rate Control Word (UCAxBRW) and eUSCI_Ax Modulation Control Word (UCAxMCTLW) regsiters.
Note: This is complicated enough that I will put into a separate video.

## Slide 49: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
14.1.2 UART Transmit on the MSP430FR2355
To configure the Tx and Rx ports, use the PxSEL1 and PxSEL0 configuration registers.

## Slide 50: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
14.1.2 UART Transmit on the MSP430FR2355
Once taken out of software reset, the eUSCI_Ax module is enabled and will wait in an idle state until information is ready to be transmitted.
A Tx is initiated by writing a byte to the eUSCI_Ax Transmit Buffer (UCAxTXBUF).
The data in UCAxTXBUF is moved into the Tx shift
register and the baud rate generator beings producing clocks.

## Slide 51: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
14.1.2 UART Transmit on the MSP430FR2355
The UCTXIFG (in UCAxIFG) flag provides the status of the transmission.
When UCTXIFG = 0, data is being shifted out and new data should not be written to the Tx buffer.
When UCTXIFG = 1, new data can be written to the Tx buffer

## Slide 52: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 14: Serial Communications in C
14.1.2 UART Transmit on the MSP430FR2355 - Configuration
www.youtube.com/c/DigitalLogicProgramming_LaMeres

## Slide 53: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 14: Serial Communications in C
14.1.2 UART Transmit on the MSP430FR2355 – Setting Baud Rate

## Slide 54: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
14.1.2 UART Transmit on the MSP430FR2355
The eUSCI_Ax peripheral has a baud rate generation circuit that can produce standard baud rates from nonstandard clock sources such as SMCLK (1MHz) and ACLK (32.768kHz).
The baud rate is set using two configuration registers, the eUSCI_Ax Baud Rate Control Word (UCAxBRW) and eUSCI_Ax Modulation Control Word (UCAxMCTLW) regsiters.

## Slide 55: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
14.1.2 UART Transmit on the MSP430FR2355

## Slide 56: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
Ex: Calculating Error of eUSCI Prescaler Devision

## Slide 57: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
Ex: Calculating Error of eUSCI Prescaler Devision

## Slide 58: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
14.1.2 UART Transmit on the MSP430FR2355
Modulation circuits dynamically add and subtract BRCLK periods to the baud rate clock that drives the shift register.
By adding small amounts of time from the BRCLK clock period to the baud rate clock, the timing error can be reduced.
In low frequency mode, the baud rate generator uses the second modulation stage to create the desired baud rate.
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 59: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
14.1.2 UART Transmit on the MSP430FR2355

## Slide 60: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
14.1.2 UART Transmit on the MSP430FR2355
Low frequency baud rate generation – used for baud rates that are less than or equal to 1/3 of BRCLK while the oversampling baud rate generation is used for higher ratios.
The UCSO16 bit in the UCAxMCTLW register controls the modulation mode with UCSO16 = 0 being for low frequency (default) and UCSO16 = 1 being for oversampling mode.
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 61: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
14.1.2 UART Transmit on the MSP430FR2355
In oversampling baud rate mode, both the first and second modulation stages are used to reduce this timing error.
The first modulation stage is configured using the UCBRFx bits within the UCAxMCTLW register.
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 62: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
14.1.2 UART Transmit on the MSP430FR2355

## Slide 63: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 14: Serial Communications in C
14.1.2 UART Transmit on the MSP430FR2355 – Setting Baud Rate
www.youtube.com/c/DigitalLogicProgramming_LaMeres

## Slide 64: The Analog Discovery 2
Brock J. LaMeres, Ph.D.
Introduction to the AD2 + Installing Waveforms

## Slide 65: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 14: Serial Communications in C
14.1.2 UART Transmit on the MSP430FR2355 – Example: Transmitting a Byte over UART at 115,200 Baud

## Slide 66: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
Ex: Transmitting a Byte Over UART at 115200 Baud

## Slide 67: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
Ex: Transmitting a Byte Over UART at 115200 Baud
To get to 115200, we need to use SMCLK

## Slide 68: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
Ex: Transmitting a Byte Over UART at 115200 Baud

## Slide 69: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
Ex: Transmitting a Byte Over UART at 115200 Baud

## Slide 70: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
Ex: Transmitting a Byte Over UART at 115200 Baud
Notice:
- The entire UCA1BRW register holds the prescalar value.
That’s why UCA1BRW = 8;

## Slide 71: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
Ex: Transmitting a Byte Over UART at 115200 Baud
Notice:
- The entire UCA1BRW register holds the prescalar value.
That’s why UCA1BRW = 8;

## Slide 72: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
Ex: Transmitting a Byte Over UART at 115200 Baud

## Slide 73: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
Ex: Transmitting a Byte Over UART at 115200 Baud
Notice:
- UCOS16 = 0 (low freq)
- UCBRFx = not used
- UCBRSx = xD6
That’s why
UCA1MCTLW = xD600

## Slide 74: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
Ex: Transmitting a Byte Over UART at 115200 Baud
Notice:
- UCOS16 = 0 (low freq)
- UCBRFx = not used
- UCBRSx = xD6
That’s why
UCA1MCTLW = xD600

## Slide 75: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
Ex: Transmitting a Byte Over UART at 115200 Baud
We will use many of the default framing options.

## Slide 76: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
Ex: Transmitting a Byte Over UART at 115200 Baud
The settings out of reset give us:
No parity
LSB First
8-Bit Length
1 Stop Bit

## Slide 77: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
Ex: Transmitting a Byte Over UART at 115200 Baud
This pin is brought out to a pin on J101

## Slide 78: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
Ex: Transmitting a Byte Over UART at 115200 Baud
After the UART and Pin is setup, we can just write to the Tx Buffer and it will automatically shift out following the UART standard.

## Slide 79: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
Ex: Transmitting a Byte Over UART at 115200 Baud
Step 1: In CCS, create a new C/C++ Empty Project (with main.c) titled:
C_UART_Tx1_Sending_Byte_at_115200
Step 2: Type in the following code in main.c after the statement to stop the watchdog timer.
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 80: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
Ex: Transmitting a Byte Over UART at 115200 Baud

## Slide 81: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
Ex: Transmitting a Byte Over UART at 115200 Baud
Step 3: Debug your program and run it.
Note: We will first look at the Tx signal with an oscilloscope. If you don’t have an oscilloscope, we will look at the signal in a different way in a later example.
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 82: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
Ex: Transmitting a Byte Over UART at 115200 Baud
Step 4: Observe the UART with an oscilloscope. Remove the jumper on the pins labeled “TXD>>” on the J101 header of the MSP430FR2355 board. Probe the pin nearest the MSP430 MCU (MSP1). This pin is being driven by UCA1TXD.
Step 5: Configure the oscilloscope waveform to center the UART frame. Measure the bit period of one of the short pulses.
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 83: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
Ex: Transmitting a Byte Over UART at 115200 Baud

## Slide 84: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 14: Serial Communications in C
14.1.2 UART Transmit on the MSP430FR2355 – Example: Transmitting a Byte over UART at 115,200 Baud
www.youtube.com/c/DigitalLogicProgramming_LaMeres

## Slide 85: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 14: Serial Communications in C
14.1.2 UART Transmit on the MSP430FR2355 – Example: Transmitting a Byte over UART at 9600 Baud

## Slide 86: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
Ex: Transmitting a Byte Over UART at 9600 Baud

## Slide 87: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
Ex: Transmitting a Byte Over UART at 9600 Baud

## Slide 88: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
Ex: Transmitting a Byte Over UART at 9600 Baud
Notice:
- UCOS16 = 0 (low freq)
- UCBRFx = not used
- UCBRSx = x92
That’s why
UCA1MCTLW = x9200
UCA1BRW = 3;

## Slide 89: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
Ex: Transmitting a Byte Over UART at 9600 Baud
UCA1BRW = 8;
UCA1MCTLW = x9200
UCSSEL = UCSSEL__ACLK

## Slide 90: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
Ex: Transmitting a Byte Over UART at 9600 Baud
We will use many of the default framing options.

## Slide 91: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
Ex: Transmitting a Byte Over UART at 9600 Baud
The settings out of reset give us:
No parity
LSB First
8-Bit Length
1 Stop Bit

## Slide 92: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
Ex: Transmitting a Byte Over UART at 9600 Baud
A1 Tx is brought out to a pin on J101

## Slide 93: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
Ex: Transmitting a Byte Over UART at 9600 Baud
After the UART and Pin is setup, we can just write to the Tx Buffer and it will automatically shift out following the UART standard.

## Slide 94: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
Ex: Transmitting a Byte Over UART at 9600 Baud
Step 1: In CCS, create a new C/C++ Empty Project (with main.c) titled:
C_UART_Tx2_Sending_Byte_at_9600
Step 2: Type in the following code in main.c after the statement to stop the watchdog timer.
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 95: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
Ex: Transmitting a Byte Over UART at 9600 Baud

## Slide 96: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
Ex: Transmitting a Byte Over UART at 9600 Baud
Step 3: Debug your program and run it.
Note: We will first look at the Tx signal with an oscilloscope. If you don’t have an oscilloscope, we will look at the signal in a different way in a later example.
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 97: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
Ex: Transmitting a Byte Over UART at 9600 Baud
Step 4: Observe the UART with an oscilloscope. Remove the jumper on the pins labeled “TXD>>” on the J101 header of the MSP430FR2355 board. Probe the pin nearest the MSP430 MCU (MSP1). This pin is being driven by UCA1TXD.
Step 5: Configure the oscilloscope waveform to center the UART frame. Measure the bit period of one of the short pulses.
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 98: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
Ex: Transmitting a Byte Over UART at 9600 Baud

## Slide 99: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 14: Serial Communications in C
14.1.2 UART Transmit on the MSP430FR2355 – Example: Transmitting a Byte over UART at 9600 Baud
www.youtube.com/c/DigitalLogicProgramming_LaMeres

## Slide 100: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 14: Serial Communications in C
14.1.2 UART Transmit on the MSP430FR2355 – Example: Sending ASCII Characters to a Terminal

## Slide 101: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 14: Serial Communications in C
14.1.2 UART Transmit on the MSP430FR2355 – Example: Sending ASCII Characters to a Terminal

## Slide 102: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
14.1.2 UART Transmit on the MSP430FR2355
Terminal – a way to communicate with a device using standard I/O on a computer.
A terminal uses the UART interface to send and receive bytes through a serial port on a computer.
The CCS design environment contains a built-in terminal feature that can be used to view data coming from the MSP430FR2355 board and also send information to the MCU board.
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 103: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
14.1.2 UART Transmit on the MSP430FR2355
The board contains a debug chip that handles downloading programs onto the MCU in addition to debugging programs.
When setting up a terminal connection to the MSP430FR2355 board, the com port number of the Application UART1 is used as the connection ID
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 104: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
14.1.2 UART Transmit on the MSP430FR2355

## Slide 105: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
14.1.2 UART Transmit on the MSP430FR2355
ASCII – a coding scheme that uses terminal windows interface with the standard I/O of the computer
ASCII – American Standard Code for Information Interchange
This coding approach allows each button press on a computer’s keyboard to result in an 8-bit code being generated and understood by the computer’s CPU.
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 106: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
14.1.2 UART Transmit on the MSP430FR2355
When writing a program, the data type “char” can be used to declare variable and store characters in ASCII.
In C, when a statement such as char Var1 = ‘A’; is used, it will assign the ASCII code for the symbol “A” into the 8-bit variable labeled “Var1.”
Using the char datatype allows us to create programs that can send and receive ASCII characters using a terminal.
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 107: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
14.1.2 UART Transmit on the MSP430FR2355

## Slide 108: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
Ex: Transmitting a Character Over UART

## Slide 109: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
Ex: Transmitting a Character Over UART
Step 1: In CCS, create a new C/C++ Empty Project (with main.c) titled:
C_UART_Tx3_Sending_Char
Step 2: Type in the following code in main.c after the statement to stop the watchdog timer.
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 110: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
Ex: Transmitting a Character Over UART

## Slide 111: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
Ex: Transmitting a Character Over UART
Step 3: Debug your program and run it.
Note: We will first look at the Tx signal with an oscilloscope to view the ASCII code for ‘A’. We will then look at the character using a terminal window.
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 112: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
Ex: Transmitting a Character Over UART
Step 4: Observe the UART with an oscilloscope. Remove the jumper on the pins labeled “TXD>>” on the J101 header of the MSP430FR2355 board. Probe the pin nearest the MSP430 MCU (MSP1). This pin is being driven by UCA1TXD.
Step 5: Configure the oscilloscope waveform to center the UART frame.
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 113: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
Ex: Transmitting a Character Over UART

## Slide 114: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
Ex: Transmitting a Character Over UART
Step 6: Now let’s launch a terminal within CCS and observe the ASCII character arrive. In CCS, use the pull down menu View → Terminal. A terminal tab will appear within CCS (usually in the lower right corner along with the “Problems” and “Advice” tabs).
Step 7: Configure the terminal window. Click on the “Open a Terminal” button on the terminal tab. This will bring up a configuration window. You will need to determine the Application UART1’s com port on your computer. On Windows, this can be found using “Device Manager → Ports (COM & LPT)”. Configure the terminal to use this com port number with a baud rate of 115200, a data size of 8, no parity, and 1 stop bit. Leave the encoding at its default value.
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 115: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
Ex: Transmitting a Character Over UART
Step 8: Plug your jumper back into the MSP430FR2355 board and observe the character ‘A’ arrive.

## Slide 116: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 14: Serial Communications in C
14.1.2 UART Transmit on the MSP430FR2355 – Example: Sending ASCII Characters to a Terminal
www.youtube.com/c/DigitalLogicProgramming_LaMeres

## Slide 117: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 14: Serial Communications in C
14.1.2 UART Transmit on the MSP430FR2355 – Example: Sending a String to a Terminal

## Slide 118: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
Ex: Transmitting a String Over UART

## Slide 119: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
Ex: Transmitting a String Over UART
Step 1: In CCS, create a new C/C++ Empty Project (with main.c) titled:
C_UART_Tx4_Sending_String
Step 2: Type in the following code in main.c after the statement to stop the watchdog timer.
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 120: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
Ex: Transmitting a String Over UART

## Slide 121: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
Ex: Transmitting a String Over UART
Step 3: Debug your program and run it.
Note: We will first look at the Tx string using the terminal window within CCS.
Step 4: Launch a terminal within CCS and observe the string arrive continually. Configure the terminal to use the com port of the Application UART1 with a baud rate of 115200, a data size of 8, no parity, and 1 stop bit. Leave the encoding at its default value. You should see “Hello World” arrive continually on the terminal.
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 122: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
Ex: Transmitting a String Over UART

## Slide 123: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 14: Serial Communications in C
14.1.2 UART Transmit on the MSP430FR2355 – Example: Sending a String to a Terminal
www.youtube.com/c/DigitalLogicProgramming_LaMeres

## Slide 124: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 14: Serial Communications in C
14.1.2 UART Transmit on the MSP430FR2355 – Example: Using Tx IRQs to Control UART Transmission

## Slide 125: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
14.1.2 UART Transmit on the MSP430FR2355
One of the drawbacks of the prior examples was that delay loops were needed to space out when data was put into the Tx buffer.
The eUSCI UART contains a variety of flags that aid in monitoring the status of the link.
These flags can also trigger IRQs.
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 126: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
14.1.2 UART Transmit on the MSP430FR2355

## Slide 127: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
14.1.2 UART Transmit on the MSP430FR2355
Transmit Interrupt (UCTXIFG):
  Flag is cleared when the Tx buffer data is written to.
  Flag is set when the Tx buffer data has been moved to the shift register and the buffer is empty.
  Only indicates that the Tx buffer is empty, not that the last character has been fully shifted out.
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 128: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
14.1.2 UART Transmit on the MSP430FR2355
Transmit Complete Interrupt (UCTXCPTIFG):
  Flag is set when the entire byte in in Tx shift register has been shifted out and it is ready for a new character.
The two Tx IRQs are enabled with the UCTXIE and UCTXCPTIE bits with in the UCAxIE
The eUSCI_Ax peripheral only contains one interrupt vector address for all the interrupts within the system.
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 129: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
14.1.2 UART Transmit on the MSP430FR2355

## Slide 130: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
14.1.2 UART Transmit on the MSP430FR2355

## Slide 131: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
14.1.2 UART Transmit on the MSP430FR2355
Each of the 4x eUSCI systems have a dedicate interrupt vector.

## Slide 132: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
Ex: Controlling UART Transmission With Interrupts

## Slide 133: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
Ex: Controlling UART Transmission With Interrupts
Step 1: In CCS, create a new C/C++ Empty Project (with main.c) titled:
C_UART_Tx5_Sending_String_using_UCTXCPTIFG
Step 2: Type in the following code in main.c after the statement to stop the watchdog timer.
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 134: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
Ex: Controlling UART Transmission With Interrupts

## Slide 135: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
Ex: Controlling UART Transmission With Interrupts

## Slide 136: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
Ex: Controlling UART Transmission With Interrupts
Step 3: Save and debug your program. Run and then terminate your program. Your program will be running but CCS will not be sharing the USB connection between the debugger and Application UART1.
Step 4: Launch a terminal within CCS and configure it to communicate with the MSP430FR2355 board.

## Slide 137: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 14: Serial Communications in C
14.1.2 UART Transmit on the MSP430FR2355 – Example: Using Tx IRQs to Control UART Transmission
www.youtube.com/c/DigitalLogicProgramming_LaMeres

## Slide 138: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 14: Serial Communications in C
14.1.3 UART Receive on the MSP430FR2355 – Overview

## Slide 139: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
14.1.3 UART Receive on the MSP430FR2355

## Slide 140: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
14.1.3 UART Receive on the MSP430FR2355
The same clock generator is used for both the Tx and Rx circuits and is configured using the UCAxBRW and UCAxMCTLW registers.
The Rx baud rate generator is configured with the desired baud rate, and the system automatically handles creating the oversampling clock for the Rx shift register.

## Slide 141: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
14.1.3 UART Receive on the MSP430FR2355
The Rx system is very similar to the Tx system in that it contains a shift register that receives the serial data.

## Slide 142: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
14.1.3 UART Receive on the MSP430FR2355
Once the frame has been received, it is put into the Rx receiver buffer (UCAxRXBUF).
Notice the framing options have to be the same as how the Tx is setup.

## Slide 143: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
14.1.3 UART Receive on the MSP430FR2355

## Slide 144: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
14.1.3 UART Receive on the MSP430FR2355
The Rx system has a state machine that monitors the incoming data and creates status flags that can be used to generate interrupts.
You never know when data will come in, so you always use flags/IRQs for Rx.

## Slide 145: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
14.1.3 UART Receive on the MSP430FR2355
Receive interrupt (UCRXIFG):
  Triggers when a new character has been received and the data is available in the Rx buffer.
  Cleared when the Rx buffer is read.
  UCRXIFG has its own flag and local IRQ enable.

## Slide 146: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
14.1.3 UART Receive on the MSP430FR2355
Start bit interrupt (UCSTTIFG)
  Triggers when the system sees a HIGH-to-LOW transition on the Rx pin indicating a new frame is being received.
  UCSTTIFG has its own flag and local IRQ enable.

## Slide 147: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
14.1.3 UART Receive on the MSP430FR2355
The Rx IRQs share the same eUSCI vector as the Tx IRQs.

## Slide 148: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
14.1.3 UART Receive on the MSP430FR2355

## Slide 149: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 14: Serial Communications in C
14.1.3 UART Receive on the MSP430FR2355 – Overview
www.youtube.com/c/DigitalLogicProgramming_LaMeres

## Slide 150: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 14: Serial Communications in C
14.1.3 UART Receive on the MSP430FR2355 – Example: Toggling LED1 Based on Terminal Keystrokes

## Slide 151: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
Ex: Receiving Characters on the eUSCI_A1 UART

## Slide 152: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
Ex: Receiving Characters on the eUSCI_A1 UART
Step 1: In CCS, create a new C/C++ Empty Project (with main.c) titled:
C_UART_Rx1_Toggling_LED1
Step 2: Type in the following code in main.c after the statement to stop the watchdog timer.
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 153: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
Ex: Receiving Characters on the eUSCI_A1 UART

## Slide 154: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
Ex: Receiving Characters on the eUSCI_A1 UART
Step 3: Save and debug your program. Run and then terminate your program. Your program will be running but CCS will not be sharing the USB connection between the debugger and Application UART1.
Step 4: Launch a terminal within CCS and configure it to communicate with the MSP430FR2355 board.

## Slide 155: Ch. 14: Serial Communication in C
14.1 Universal Asynchronous Receiver/Transmitter (UART) Operation
Ex: Receiving Characters on the eUSCI_A1 UART
Can you see these ASCII codes in the debugger?

## Slide 156: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 14: Serial Communications in C
14.1.3 UART Receive on the MSP430FR2355 – Example: Toggling LED1 Based on Terminal Keystrokes
www.youtube.com/c/DigitalLogicProgramming_LaMeres