## Slide 1: Reconfigurable Computing & Its Use in Space Applications in 10 minutes…
Dr. Brock J. LaMeres
Associate Professor
Department of Electrical & Computer Engineering

## Slide 2: What is Reconfigurable Computing
A System That Alters Its Hardware as its Normal Operating Procedure
  This can be done in real-time or at compile time.
  This can be done on the full-chip, or just on certain portions.
  Changing the hardware allows it to be optimized for the application at hand.
Today’s Computers are Based on a General-Purpose Processor
  The GP CPU is designed to do many things.
  This is the “Jack of All Trades, Master of None” approach.
General Purpose CPU Model
Reconfigurable Computing Model

## Slide 3: Who Cares?
Our Existing Computers Seem to be Working Well. Why Change?
  Our existing computers have benefited from 40 years of Moore’s Law.
  In the 1960’s, Gordon Moore predicted that the number of transistors on a chip would double every ~24 months.
Gordon Moore, co-founder of Intel, holding a vacuum tube.
1959 - 1965
1971* - 2011
Note: First microprocessor introduced in 1971,
the Intel 4004 with 2300 transistors.
Intel 4004 (2300 T)
Intel Xeon (2B T)

## Slide 4: How long can we do this?
When will Moore’s Law End?
  Most exponentials do come to an end.
Clock Speed
Power
Performance per Clock Cycle
But is transistor count what we care about?

## Slide 5: Computation vs. Transistor Count
We Really Care About Computation
You Are Here

## Slide 6: The Promise of RC
A Computer Always Needs an Application
  We discovered that space computers could be greatly enhanced by RC.
  They need to be light. RC reuses hardware, that saves mass.

## Slide 7: The Promise of RC
A Computer Always Needs an Application
  We discovered that space computers could be greatly enhanced by RC.
  They need to be light. RC reuses hardware, that saves mass.
  They need to be low power. RC eliminates unnecessary circuitry.

## Slide 8: The Promise of RC
A Computer Always Needs an Application
  We discovered that space computers could be greatly enhanced by RC.
  They need to be light. RC reuses hardware, that saves mass.
  They need to be low power. RC eliminates unnecessary circuitry.
  They need to have high computation. RC can do that.

## Slide 9: The Promise of RC
A Computer Always Needs an Application
  We discovered that space computers could be greatly enhanced by RC.
  They need to be light. RC reuses hardware, that saves mass.
  They need to be low power. RC eliminates unnecessary circuitry.
  They need to have high computation. RC can do that.
  They need to operate in the presence of harsh radiation.
Can you repeat the question???

## Slide 10: Where Does Radiation Come From?
3) Trapped Radiation
1) Cosmic Rays
2) Solar Particle Events

## Slide 11: What are the Effects?
1. Total Ionizing Dose (TID)
      Cumulative long term damage due to ionization.
      Primarily due to low energy protons and electrons due to higher, more constant flux, particularly when trapped
      Problem #1 – Oxide Breakdown
        Threshold Shifts
        Leakage Current
        Timing Changes
2. Single Event Effects (SEE)
      Electron/hole pairs created by a single particle passing through semiconductor
      Primarily due to heavy ions and high energy protons
      Excess charge carriers cause current pulses
      Creates a variety of destructive and non-destructive damage “Critical Charge” = the amount of charge deposited to change the state of a gate

## Slide 12: But I’m Texting Right Now?
How can our computers function?
You Are Here
Thank you atmosphere. Thank you magnetosphere

## Slide 13: But there are computers in space?
Stuff is in space now, how does it function?
Rad-Hard Processors Can be Made that are SLOW and EXPENSIVE
  Rad-Hard computers tend to lag commercial versions in performance by 10+ years.
  They are also 100s-1000x more expensive.
Thank you federal government.
A-Side Computer
BAE Rad750 $200,000
B-Side Computer
BAE Rad750 $200,000

## Slide 14: I Know You’re Going to Ask….
Can’t you just add shielding?
  Shielding helps for protons and electrons <30MeV, but has diminishing returns after 0.25”.
  This shielding is typically inherent in the satellite/spacecraft design, meaning the most optimal amount of shielding is usually present in the shell of the spacecraft.
Shield Thickness vs. Dose Rate (LEO)

## Slide 15: How Does RC Help This?
Total Ionizing Dose
  TID actually diminishes as features get smaller.
  This is good because we want to use the smallest transistors to get the fastest performance.
  Using off-the-shelf parts also reduces cost.
Single Event Effects
  SEE gets worse! But it isn’t permanent.
  So we just need a new computer architecture to handle it.

## Slide 16: Enter MSU
FPGA-Based, Radiation Tolerant Computer
  The FPGA is divided up into Tiles
  A Tile is a quantum of resources that:
      Fully contains a system (e.g., processor, accelerator)
      Can be programmed via partial reconfiguration (PR)
Fault Tolerance
  TMR + Spares
  Spatial Avoidance of Background Repair
  Scrubbing
  An External Radiation Sensor
16 Tile System on an Xilinx Virtex-6

## Slide 17: Technical Readiness Level (TRL-1)
Step 1 – Understand the Problem and See if RC Helps
  The Montana Space Grant Consortium funds an investigation into conducting radiation tolerant computing research at MSU. The goal is to understand the problem, propose a solution, and build relationships with scientists at NASA.
(2008-2010)
2010
2011
2012
2013
2014
2015
2016
Proof of Concept
2009
2008
Timeline of Activity at MSU
Clint Gauer (MSEE from MSU 2009) demo’s computer to MSFC Chief of Technology Andrew Keys

## Slide 18: Technical Readiness Level (TRL-3)
Step 2 – Build a Prototype and Test in a Cyclotron
  NASA funds the development of a more functional prototype and testing under bombardment by radiation at the Texas A&M Radiation Effects Facility.
(2008-2010)
2010
2011
2012
2013
2014
2015
2016
Proof of Concept
Prototype Development & Cyclotron Testing
(2010-2012)
2009
2008
Timeline of Activity at MSU
Ray Weber (Ph.D., EE from MSU, 2014) prepares experiment.

## Slide 19: Technical Readiness Level (TRL-5)
Step 3 – Demonstrate as Flight Hardware on High Altitude Balloons
  NASA funds the development of the computer into flight hardware for demonstration on high altitude balloon systems, both in Montana and at NASA.
(2008-2010)
2010
2011
2012
2013
2014
2015
2016
Proof of Concept
Prototype Development & Cyclotron Testing
High Altitude Balloon Demos
(2010-2012)
(2011-2013)
2009
2008
Timeline of Activity at MSU
MSU Computer
Justin Hogan (Ph.D., EE from MSU, 2014) prepares payload.

## Slide 20: Technical Readiness Level (TRL-7)
Step 4 – Demonstrate as Flight Hardware on a Sounding Rocket
  NASA funds the demonstration of the computer system on sounding rocket.
  Payload is integrated and will fly on 10/20/14 at White Sands Missile Range.
(2008-2010)
2010
2011
2012
2013
2014
2015
2016
Proof of Concept
Prototype Development & Cyclotron Testing
High Altitude Balloon Demos
Sounding Rocket Demo
(2010-2012)
(2011-2013)
(2012-2014)
2009
2008
Timeline of Activity at MSU
Justin Hogan and
Ray Weber
(MSU Ph.D. Grads) at rocket training boot camp in 2012.

## Slide 21: Technical Readiness Level (TRL-8)
Step 5 – Demonstrate on the International Space Station
  NASA funds the demonstration of computer system in International Space Station.
(2008-2010)
2010
2011
2012
2013
2014
2015
2016
Proof of Concept
Prototype Development & Cyclotron Testing
High Altitude Balloon Demos
Sounding Rocket Demo
ISS
Demo
(2010-2012)
(2011-2013)
(2012-2014)
(2014-2015)
2009
2008
Timeline of Activity at MSU
ISS Mockup at Johnson Space Center for Crew Training
Mission Control Room for Apollo Program

## Slide 22: Technical Readiness Level (TRL-8)
Selfie with $60M Space Suit

## Slide 23: Technical Readiness Level (TRL-9)
Step 6 – Demonstrate as a Stand-Alone Satellite
  NASA funds the demonstration of the computer system in a Low Earth Orbit mission.
(2008-2010)
2010
2011
2012
2013
2014
2015
2016
Proof of Concept
Prototype Development & Cyclotron Testing
High Altitude Balloon Demos
Sounding Rocket Demo
ISS
Demo
Satellite
Demo
(2010-2012)
(2011-2013)
(2012-2014)
(2014-2015)
(2014-2016)
2009
2008
Timeline of Activity at MSU

## Slide 24: Technical Readiness Level (TRL-9)
Step 7 – Commercialize It
  License Agreement with 406 Aerospace, LLC, Bozeman, MT.

## Slide 25: Collaborators
Faculty & Scientists
  Todd Kaiser, MSU Electrical & Computer Engineering Department
  Ross Snider, MSU Electrical & Computer Engineering Department
  Hunter Lloyd, MSU Computer Science Department
  Robb Larson, MSU Mechanical & Industrial Engineering Department
  Angela Des Jardins, MSU Physics Department & MSGC
  Randy Larimer, MSU Electrical Engineering Department & MSGC
  Berk Knighton, MSU Chemistry Department & MSGC
  David Klumpar, MSU Physics Department & SSEL
  Larry Springer, MSU Physics Department & SSEL
  Ehson Mosleh, MSU Physics Department & SSEL
  Gary Crum, NASA Goddard Space Flight Center
  Thomas Flatley, NASA Goddard Space Flight Center
  Leroy Hardin, NASA Marshall Space Flight Center
  Kosta Varnavas, NASA Marshall Space Flight Center
  Andrew Keys, NASA Marshall Space Flight Center
  Robert Ray, NASA Marshall Space Flight Center
  Leigh Smith, NASA Marshall Space Flight Center
  Eric Eberly, NASA Marshall Space Flight Center
  Alan George, University of Florida & NSF Center for High Performance Reconfig Comp.

## Slide 26: Students
Everything was Designed and Built By MSU Students!
Todd Buerkle, Justin Hogan, Ray Weber at Johnson Space Center for demo, 2012.
Todd Buerkle, Jennifer Hane at the Marshall Space Flight Center, 2011.
Justin Hogan at the NASA Columbia Scientific Balloon Facility, 2012.
Justin Hogan & Ray Weber featured in MSU News Story, 2012.
Clint Gauer demo’s computer at Marshall Space Flight Center, 2009.
Todd Buerkle & Jennifer Hane demo computer at Marshall Space Flight Center, 2012.
Clint Gauer at Marshall Space Flight Center for demo, 2009.
Kaysha Young prepares payload for balloon flight, 2012.
2013 balloon team recovers payload in front of moose, 2013.
2011 balloon team featured in MSU news story, 2011.

## Slide 27
Thank You For Not
Asking Questions