## Slide 1: CyberShield Intrusion Tolerant Flight Computing Through Hardware Obfuscation
Product Security Community Technical Exchange
December 15, 2022

## Slide 2: Motivation
Types of Cybersecurity Attacks
Inserting malicious code into the computer’s program memory and tricking the processor into executing it.

## Slide 3: Motivation
Our Focus - Malware on Flight Computers
  High Value Assets
  Willing to trade SWaP for reliability
Key Characteristics
  Embedded Edge Computers
    Dedicated software, not general-purpose.
    Smaller (sometimes 8-pin packages)
    Lower Clock Frequencies (1MHz - 50MHz)
    Smaller memories (256k to 1M)
    Often no OS other than real-time scheduler.
Missiles (RMD Patriot)
UAS (RIS GPS OCX)
USA (RMD Patriot)

## Slide 4: Hardware Obfuscation to Defeat Malware
The Malware Cybersecurity Challenge
The nation’s cyber infrastructure consists of a massive number of identical computer systems.
This homogeneity is advantageous because a single piece of software can be deployed across millions of systems to increase capacity.

## Slide 5: Hardware Obfuscation to Defeat Malware
The Malware Cybersecurity Challenge
The nation’s cyber infrastructure consists of a massive number of identical computer systems.
This homogeneity is advantageous because a single piece of software can be deployed across millions of systems to increase capacity.
  However, this gives an attacker a significant advantage in terms of effort relative to system defenders by re-using their attack across numerous systems.

## Slide 6: Hardware Obfuscation to Defeat Malware
This is True in Edge Computers Too…
We want to take advantage of the power of modern software development tools and hardware abstraction but that means
We use edge computers with architectures that can be studied by attackers.
SpaceX Starlink (46 satellites with identical edge computers)

## Slide 7: Hardware Obfuscation to Defeat Malware
If Homogeneity gives attackers an advantage, let’s obfuscate.
Take Away the Attacker’s Advantage by Randomizing the Hardware

## Slide 8: Hardware Obfuscation to Defeat Malware
Practical Considerations
  Changing custom hardware takes years.
  We still need to take advantage of modern dev tools.

## Slide 9: Hardware Obfuscation to Defeat Malware
Practical Considerations
  Changing custom hardware takes years.
  We still need to take advantage of modern dev tools.
What if we use FPGAs?
  A programmable logic device.
  Now fast enough to meet edge computing needs.
  Can implement full computer systems on a single chip.
  The “hardware” is simply a text description fed into a synthesis tool.
Synthesis / Implementation

## Slide 10: Hardware Obfuscation to Defeat Malware
Ok, so now we can change hardware, but how to obfuscate?

## Slide 11: Hardware Obfuscation to Defeat Malware
Ok, so now we can change hardware, but how to obfuscate?
  If we can re-assign the instruction codes that the CPU can execute, an attacker’s malware won’t be executable.

## Slide 12: Hardware Obfuscation to Defeat Malware
Ok, so now we can change hardware, but how to obfuscate?
  If we can re-assign the instruction codes that the CPU can execute, an attacker’s malware won’t be executable.
We simply change the instruction code lookup table in the CPU.

## Slide 13: Hardware Obfuscation to Defeat Malware
Ok, so now we can change hardware, but how to obfuscate?
  If we can re-assign the instruction codes that the CPU can execute, an attacker’s malware won’t be executable.
We simply change the instruction code lookup table in the CPU.
But then it won’t recognize our own code?

## Slide 14: Hardware Obfuscation to Defeat Malware
Ok, so now we can change hardware, but how to obfuscate?
  If we can re-assign the instruction codes that the CPU can execute, an attacker’s malware won’t be executable.
We simply change the instruction code lookup table in the CPU.
But then it won’t recognize our own code?
But we can control that too…

## Slide 15: Hardware Obfuscation to Defeat Malware
CyberShield Concept
  Compile-time creation of obfuscated computing hardware.

## Slide 16: Hardware Obfuscation to Defeat Malware
CyberShield Concept
  Compile-time creation of obfuscated computing hardware.
  But what if the attacker guesses our instruction codes?

## Slide 17: Hardware Obfuscation to Defeat Malware
CyberShield Concept
  Compile-time creation of obfuscated computing hardware.
  But what if the attacker guesses our instruction codes?
  What if we had TWO computers with different instruction code assignments? Then we could compare opcodes between the computers and if the are ever the SAME, it is malware.

## Slide 18: Hardware Obfuscation to Defeat Malware
CyberShield Concept
  Compile-time creation of obfuscated computing hardware.
  But what if the attacker guesses our instruction codes?
  What if we had TWO computers with different instruction code assignments? Then we could compare opcodes between the computers and if the are ever the SAME, it is malware.
We can do that!
We can do that!

## Slide 19: Hardware Obfuscation to Defeat Malware
CyberShield Concept
  Compile-time creation of obfuscated computing hardware.
  But what if the attacker guesses our instruction codes?
  What if we had TWO computers with different instruction code assignments? Then we could compare opcodes between the computers and if the are ever the SAME, it is malware.
We can do that!
We can do that!

## Slide 20: Hardware Obfuscation to Defeat Malware
CyberShield Concept
  Compile-time creation of obfuscated computing hardware.
  But what if the attacker guesses our instruction codes?
  What if we had TWO computers with different instruction code assignments? Then we could compare opcodes between the computers and if the are ever the SAME, it is malware.
We can do that!
We can do that!
X

## Slide 21: Hardware Obfuscation to Defeat Malware
CyberShield Concept
  Compile-time creation of obfuscated computing hardware.
  But what if the attacker guesses our instruction codes?
  What if we had TWO computers with different instruction code assignments? Then we could compare opcodes between the computers and if the are ever the SAME, it is malware.
We can do that!
We can do that!
In fact, we can keep going..
In fact, we can keep going..

## Slide 22: Hardware Obfuscation to Defeat Malware
CyberShield Concept
  Compile-time creation of obfuscated computing hardware.
  But what if the attacker guesses our instruction codes?
  What if we had TWO computers with different instruction code assignments? Then we could compare opcodes between the computers and if the are ever the SAME, it is malware.
We can do that!
We can do that!
And going…
In fact, we can keep going..

## Slide 23: Hardware Obfuscation to Defeat Malware
CyberShield Concept
  But why add more than two cores?
Shuttle Flight Computer (4MR)

## Slide 24: Hardware Obfuscation to Defeat Malware
CyberShield Concept
  But why add more than two cores?
  That’s the flight computing part.
Missiles (RMD Patriot)
UAS (RIS GPS OCX)
USA (RMD Patriot)
Shuttle Flight Computer (4MR)

## Slide 25: Hardware Obfuscation to Defeat Malware
CyberShield Concept
  But why add more than two cores?
  That’s the flight computing part.
Redundancy for Fault Tolerance
  Triple Modular Redundancy.
  Majority vote produces the output.
  Widely used in space computers.
Missiles (RMD Patriot)
UAS (RIS GPS OCX)
USA (RMD Patriot)
Shuttle Flight Computer (4MR)

## Slide 26: Hardware Obfuscation to Defeat Malware
It turns out MSU has a History of Building Space Computers Too
RadPC
RadPC
RadPC
RadPC
RadPC
RadPC

## Slide 27: Hardware Obfuscation to Defeat Malware
CyberShield Concept with
Fault-Tolerance
  We just need to add a majority voter.
  That’s also why we are using a RISC-V CPU architecture.
QMR
RV32

## Slide 28
DEMO
of
Tool Chain

## Slide 29: Where we Are, Where we are Going
Opcode
Translator
VHDL Files
FPGA
Core 1
Core 2
Core 3
Attack
Detect
Voter
Synthesis
& Implementation
Malware Resistant Computer
FPGA Design Tools
Processor 1
Program Memory 1
Attack Detect Voter
HDL Description of System
Source Code (main.c)
Compiler
Processor Definition
(header file)
Machine Code
(object file)
OpCode Def 1
Disassembly
Processor 2
Program Memory 2
OpCode Def 2
Processor 3
Program Memory 3
OpCode Def 3
Opcode Randomization Scheme
Standard Eclipse Programming Environment Supporting C and Assembly.
Targeting a widely-used Microcontroller, the MSP430. A 16-bit RISC processor.
Testbed program (main.c) to keep a missile upright

## Slide 30: Where we Are, Where we are Going
Program Vulnerabilities (Classic Buffer Overflow Attack)
Data Memory
Address
x2000
x3000
decode_array
frequency
set_angle
rx_index
RXBUF
index
Global Variables
Stack
ISR Return Addresses
Local Variables

## Slide 31: Where we Are, Where we are Going
Program Vulnerabilities (Classic Buffer Overflow Attack)
Data Memory
Address
x2000
x3000
decode_array
frequency
set_angle
rx_index
RXBUF
index
Global Variables
Stack
ISR Return Addresses
Local Variables
1. When user sends new setpoint over UART, an IRQ triggers, stacks return address, and retrieves new value for RXBUF.
2. But the developer introduced a vulnerability by adding a delay loop in the main program to allow the UART to complete before resetting the input buffer size back to 0.
2. But the developer introduced a vulnerability by adding a delay loop in the main program to allow the UART to complete before resetting the input buffer size back to 0.
3. This allows the attacker to stream in malicious code and replace the correct ISR return address.
NOP
NOP
NOP
Malware
Malware
Malware
Malware
NOP
NOP
NOP
New ISR Return Addr
Bad Set Angle
2. But the developer introduced a vulnerability by adding a delay loop in the main program to allow the UART to complete before resetting the input buffer size back to 0.

## Slide 32: Where we Are, Where we are Going
Program Vulnerabilities (Classic Buffer Overflow Attack)
Data Memory
Address
x2000
x3000
decode_array
frequency
set_angle
rx_index
RXBUF
index
Global Variables
Stack
ISR Return Addresses
Local Variables
1. When user sends new setpoint over UART, an IRQ triggers, stacks return address, and retrieves new value for RXBUF.
2. But the developer introduced a vulnerability by adding a delay loop in the main program to allow the UART to complete before resetting the input buffer size back to 0.
2. But the developer introduced a vulnerability by adding a delay loop in the main program to allow the UART to complete before resetting the input buffer size back to 0.
3. This allows the attacker to stream in malicious code and replace the correct ISR return address.
NOP
NOP
NOP
Malware
Malware
Malware
Malware
NOP
NOP
NOP
New ISR Return Addr
Bad Set Angle
2. But the developer introduced a vulnerability by adding a delay loop in the main program to allow the UART to complete before resetting the input buffer size back to 0.

## Slide 33: Where we Are, Where we are Going
Get the 4MR Version of CyberShield to “Operate Under Attack”
Missiles (RMD Patriot)
UAS (RIS GPS OCX)
USA (RMD Patriot)
Shuttle Flight Computer (4MR)

## Slide 34: A Story of the CyberShield History
Get the 4MR Version of CyberShield to “Operate Under Attack”
Shuttle Flight Computer (4MR)

## Slide 35
Questions