## Slide 1: A Brief Introduction to Musical Acoustics
EELE217
R.C. Maher

## Slide 2: Harmonic and Inharmonic Sounds
Musical instruments with simple oscillators usually produce periodic waveforms
Periodic waveforms have a fundamental frequency, f0, and a harmonic spectrum: spectral energy just at frequencies that are integer multiples of f0.
These harmonic components are called harmonics, overtones, or partials .
Some musical instruments produce inharmonic sounds: bells, drums, etc.

## Slide 3: Pitch
Musical sounds often have a pitch that is related to the sound’s spectral content
The pitch of a harmonic sound is usually close to the fundamental frequency of that sound
Inharmonic sounds may have a perceived pitch, but it is not merely the fundamental of some harmonic series

## Slide 4: Organization of Western Music
Two harmonic sounds with different fundamental frequencies can lead to interesting frequency coincidences among their partials
When the fundamentals have a low integer ratio relationship, this is a consonant interval

## Slide 5: Consonant Intervals
Unison 3rd 4th 5th Octave
1/1 5/4 4/3 3/2 2/1
100 125 133.33 150 200
200 250 266.67 300 400
300 375 400 450 600
400 500 533.33 600 800
500 625 666.67 750 1000
600 750 800 900 1200
700 875 933.33 1050 1400
800 1000 1066.67 1200 1600
900 1125 1200 1350 1800
1000 1250 1333.33 1500 2000
1100 1375 1466.67 1650 2200
1200 1500 1600 1800 2400
1300 1625 1733.33 1950 2600
1400 1750 1866.67 2100 2800
1500 1875 2000 2250 3000
1600 2000 2133.33 2400 3200

## Slide 6: Musical Scales and Temperament
European music is based on the notion of a diatonic pitch scale. The scale specifies the allowable musical pitches: 8 scale steps out of 12.
Problem: if integer frequency ratios are used (Just intonation), chords only sound in tune if based on fundamental (tonic) pitch. Changing musical “key” is not possible.

## Slide 7: Equal Tempered Scale
To solve the musical “key” problem, keyboard instruments now use equal-tempered tuning.
Note frequencies are distributed uniformly in a logarithmic span: fn = f0  2n/12
Just vs. equal tempered tuning:
Unison 3rd 4th 5th Octave
100 125.0000 133.3333 150.0000 200.0000
100 125.9921 133.4840 149.8307 200.0000

## Slide 8: Tuning Example

## Slide 9: Equal Temperament vs. Just
3200
2397.29
2400
2135.74
2133.33
2015.87
2000
1600
3000
2247.46
2250
2002.26
2000.00
1889.88
1875
1500
2800
2097.63
2100
1868.78
1866.67
1763.89
1750
1400
2600
1947.80
1950
1735.29
1733.33
1637.90
1625
1300
2400
1797.97
1800
1601.81
1600.00
1511.91
1500
1200
2200
1648.14
1650
1468.32
1466.67
1385.91
1375
1100
2000
1498.31
1500
1334.84
1333.33
1259.92
1250
1000
1800
1348.48
1350
1201.36
1200.00
1133.93
1125
900
1600
1198.65
1200
1067.87
1066.67
1007.94
1000
800
1400
1048.81
1050
934.39
933.33
881.94
875
700
1200
898.98
900
800.90
800.00
755.95
750
600
1000
749.15
750
667.42
666.67
629.96
625
500
800
599.32
600
533.94
533.33
503.97
500
400
600
449.49
450
400.45
400.00
377.98
375
300
400
299.66
300
266.97
266.67
251.98
250
200
200
149.83
150
133.48
133.33
125.99
125
100
2/1
1.498307
3/2
1.33484
4/3
1.259921
5/4
1/1
octave
5th
4th
3rd

## Slide 10: Rhythm
Beats per minute
Beats per measure (time signature)
Duration of musical notes specified in fractions: whole, half, quarter, eighth, sixteenth, 32nd

## Slide 11: Musical Notation
Notation specifies pitches, durations, and time evolution
Representation is like a spectrogram: frequency vs. time

## Slide 12: Standard Tuning Frequencies
C4 261.62Hz
C5 523.25Hz
C6 1046.5Hz
C3 130.81Hz
C2 65.41Hz
A4 440Hz
 ≈ 33cm
 ≈ 66cm
 ≈ 78cm
 ≈ 1.3m
 ≈ 2.6m
 ≈ 5.2m
“middle C”

## Slide 13: Musical Timbre
The relative spectral energy at different frequencies is perceived as a distinct tone color, or timbre (pronounced as either tam--burr or tim-burr)
Timbre: The combination of qualities of a sound that distinguishes it from other sounds of the same pitch and volume

## Slide 14: Musical Instruments
Almost any object can be considered a musical instrument
Most conventional musical instruments have
  an excitation source
  a vibrating element
  a resonant body
  a means of coupling the vibrations so that they radiate into the air as sound waves

## Slide 15: Musical Instruments (cont.)
The excitation is a motive force
The vibrating element usually creates many harmonics
The resonant body emphasizes some frequencies and deemphasizes others
The coupling means takes energy from the vibrating element and “loses” it (radiates) into an acoustical wave through the air

## Slide 16: Example: String Instrument
Bow or pluck excitation.
Vibrating string couples energy to the hollow wood body (resonator).
Vibrating body couples sound into the air (radiation).

## Slide 17: Example: Singing Voice
Lungs
Glottis
(vocal cords)
Resonance of the throat,
nasal passages,
and the mouth
Projection from the mouth

## Slide 18: Simulation: Excitation and Filter
Signal rich in harmonics (a “buzz”) with spectral shaping
Does it sound like singing? Does the vibrato help?