## Slide 1: Perceptual Audio Coding
Rob Maher
Department of Electrical and Computer Engineering Montana State University-Bozeman

## Slide 2: Human Auditory Performance
Auditory sensation from 20Hz to 20kHz
  Nearly 10 octaves, vs. less than 1 octave for vision, or 144-148 MHz for 2M band
Pressure sensitivity range 120dB
  At threshold of hearing, particle motion is smaller than the diameter of a hydrogen atom: any more sensitivity and we would hear thermal vibrations

## Slide 3: Nonlinear Sensitivity

## Slide 4: Frequency Masking
The Result:

## Slide 5: Critical Bandwidth
The frequency masking effect depends upon the level of the probe, and the power and bandwidth of the masker
Masking is thought to be caused by the mechanical frequency selectivity of the cochlea.
The effective frequency range of masking is referred to as a critical band.
The critical bandwidth varies with frequency:
  BW approx. 100Hz below 700Hz
  BW approx. 1/3 octave above 700Hz

## Slide 6: “Coding” of audio
Reduce redundancy: eliminate information that is predictable from other parts of the signal.
Reduce irrelevancy: eliminate information that is inaudible to a human listener.
Provide signal-dependent adaptation: incorporate a model of human auditory performance.

## Slide 7: Coding Example
Motion Picture Experts Group (MPEG) standards for video and audio.
MPEG-1: late 1980s, development of perceptual video and audio compression
MPEG-1: three different computational complexities defined, called Layer 1, Layer 2, and Layer 3
Most popular was Layer 3 == “MP3”

## Slide 8: Perceptual Audio Coder (MP3) Block Diagram
Filtered Audio Signal
Audio Input
Coding Filterbank
Quantization and Rate Control
Noiseless Coding and Bitstream Packing
Perceptual
Model
Perceptual
Threshold
Quantized filterbank values and
side information
Coded
Bitstream

## Slide 9: MP3 Example 1
Original Signal (stereo, 44.1kHz, 1.35Mbps)
Compressed 1:11 MP3 (stereo, 44.1kHz, 128kbps)
The difference between the two. This is what the coder removes as inaudible!
+12dB boost on difference:

## Slide 10: MP3 Example 2
Original Signal (stereo, 44.1kHz, 1.35Mbps)
Compressed 1:11 MP3 (stereo, 44.1kHz, 128kbps)
The difference between the two. This is what the coder removes as inaudible!
Another example: