## Slide 1: A Tutorial on Acoustical Transducers: Microphones and Loudspeakers
Robert C. Maher
Montana State University
EELE 417/517 Acoustics and Audio Engineering
Fall 2018

## Slide 2: Outline
Introduction: What is sound?
Microphones
  Principles
  General types
  Sensitivity versus Frequency and Direction
Loudspeakers
  Principles
  Enclosures
Conclusion

## Slide 3: Transduction
Transduction means converting energy from one form to another
Acoustic transduction generally means converting sound energy into an electrical signal, or an electrical signal into sound
Microphones and loudspeakers are acoustic transducers

## Slide 4
Acoustics and Psychoacoustics
Mechanical to Acoustical
Acoustical to Mechanical
Acoustical propagation (reflection, diffraction, absorption, etc.)
Mechanical to Electrical (nerve signals)
Electrical to Psychological

## Slide 5: What is Sound?
Vibration of air particles
A rapid fluctuation in air pressure above and below the normal atmospheric pressure
A wave phenomenon: we can observe the fluctuation as a function of time and as a function of spatial position

## Slide 6: Sound (cont.)
Sound waves propagate through the air at approximately 343 meters per second
  Or 1125 feet per second
  Or 4.7 seconds per mile ≈ 5 seconds per mile
  Or 13.5 inches per millisecond ≈ 1 foot per ms
The speed of sound (c) varies as the square root of absolute temperature
  Slower when cold, faster when hot
  Ex: 331 m/s at 32ºF, 353 m/s at 100ºF

## Slide 7: Sound (cont.)
Sound waves have alternating high and low pressure phases
Pure tones (sine waves) go from maximum pressure to minimum pressure and back to maximum pressure. This is one cycle or one waveform period (T).
T

## Slide 8: Wavelength and Frequency
If we know the waveform period and the speed of sound, we can compute how far the sound wave travels during one cycle. This is the wavelength (λ).
Another way to describe a pure tone is its frequency (f): how many cycles occur in one second.

## Slide 9: Wave Relationships
c = f · λ [m/s = /s · m]
T = 1/f
λ = T · c
  c = speed of sound [m/s]
  f = frequency [ /s]
  λ = wavelength [ m ]
  T = period [ s ]
  Note: high frequency implies short wavelength, low frequency implies long wavelength

## Slide 10: Sound Amplitude and Intensity
The amount of pressure change due to the sound wave is the sound amplitude
The motion of the air particles due to the sound wave can transfer energy
The rate at which energy is delivered by the wave is the sound power [ W (watts)]
The power delivered per unit area is the sound intensity [ W/m2 ]

## Slide 11: Microphone Principles
Concepts:
  Since sound is a pressure disturbance, we need a pressure gauge of some sort
  Since sound exerts a pressure, we can use it to drive an electrical generator
  Since sound is a wave, we can measure simultaneously at two (or more) different positions to figure out the direction the wave is going

## Slide 12: Microphone: Diaphragm and Generating Element
Diaphragm: a membrane that can be set into motion by sound waves
  Sensitivity: how much motion from a given sound intensity
Generating Element: an electromechanical device that converts motion of the diaphragm into an electrical current and voltage
  Sensitivity: how much electrical signal power is obtained from a given sound intensity

## Slide 13: Electrical Generators
Variable Resistor
Variable Inductor
Electromagnetic
Variable Capacitor
Piezoelectric
Other exotic methods…

## Slide 14: The First Microphones…
Alexander Graham Bell (variable resistor)
Carbon granules (variable resistor)
Battery
+
-
Acid water
Battery
+
-

## Slide 15: Ribbon Microphone
Diaphragm (metallic foil)
Magnet
Electrical Circuit
N
S

## Slide 16: Dynamic Microphone
Diaphragm moves a coil of wire through a fixed magnetic field: Faraday’s Law indicates that a voltage is produced
N
S

## Slide 17: Piezoelectric Microphone
Piezoelectric generating element: certain crystals produce a voltage when distorted (piezo means “squeeze” in Greek)
Diaphragm attached to piezo element
Rugged, reasonably sensitive, not particularly linear

## Slide 18: Capacitor (Condenser) Mic
Variable electrical capacitance
  British use the word “condenser”
Currently the best for ultra sensitivity, low noise, and low distortion (precision sound level meters use condenser mics
Difficult to manufacture, delicate, and can be too sensitive for some applications

## Slide 19: Condenser Mic (cont.)
Capacitance = charge / voltage
Capacitance ≈ ε A / d
  A = area, d=distance between plates
  ε = permittivity
signal voltage ≈ d · (charge / (ε · A))
constant
Backplate
Diaphragm
High impedance preamp

## Slide 20: Microphone Patterns
A single diaphragm acts like a pressure detector
Two diaphragms can give a directional preference
Placing the diaphragm in a tube or cavity can also give a directional preference

## Slide 21: Microphone Patterns (cont.)
Omnidirectional: all directions
Unidirectional or Cardioid: one direction
Bi-directional or ‘figure 8’: front and back pickup, side rejection

## Slide 22: Microphone Coloration
Most microphones are not equally sensitive at all frequencies
  The human ear is not equally sensitive at all frequencies either!
The frequency (and directional) irregularity of a microphone is called coloration
Example: Stereophile Microphone .wav

## Slide 23: Loudspeakers

## Slide 24: Loudspeakers
Diaphragm attached to a motor element
Diaphragm motion is proportional to the electrical signal (audio signal)
Efficiency: how much acoustical power is produced from a given amount of input electrical power

## Slide 25: Moving Coil Driver
Cone
Magnet
Voice Coil
Speaker Frame
Current through coil creates a magnetic force relative to the fixed magnet

## Slide 26: Mechanical Challenges
Large diameter diaphragm can produce more acoustic power, but has large mass and directional effects
Diaphragm displacement (in and out) controls sound intensity, but large displacement causes distortion
Result: low frequencies require large diameter and large displacement

## Slide 27: Unbaffled Driver
Air has time to “slosh” between front and back at low frequencies: poor bass response

## Slide 28: Baffled Driver (flush mount)
Baffle prevents front-back interaction: improved low frequency performance

## Slide 29: Loudspeaker Enclosure
Enclosure is a key part of the acoustical system design
Sealed box or acoustic suspension
  enclosed air acts like a spring
Vented box or bass-reflex
  enclosed air acts like a resonator
Horns and baffles

## Slide 30: Acoustic Suspension
Sealed box acts as a stiff “air spring”
Enclosed volume chosen for optimum restoring force
Relatively weak (compliant) cone suspension
Greatly reduced nonlinear distortion!

## Slide 31: Ported (Resonant) Enclosure
Port (hole): radiates only at frequencies near box resonant frequency, but reduces cone motion.
Ported box is a Helmholtz resonator.
Enclosed volume and port size chosen to boost acoustic efficiency at low frequencies: reduces required cone motion for a given output, allowing lower distortion.
Driver acts as a direct radiator at frequencies above box resonance.

## Slide 32: Other Loudspeaker Issues
Multi-way loudspeakers: separate driver elements optimized for low, mid, and high frequencies (woofer, squawker, tweeter)
Horns: improve acoustical coupling between driver and the air
Transmission line enclosures
Electrostatic driver elements
‘Powered’ speakers

## Slide 33: Conclusions
Microphone: a means to sense the motion of air particles and create a proportional electrical signal
Loudspeaker: a means to convert an electrical signal into proportional motion of air particles
Engineering tradeoffs exist: there is not a single best solution for all situations